## Slide 1: Safety Alert: Incident CAPW-075-2008 Waste Materials found on Cable Trays - Potential Dropped Objects
October 2008

## Slide 2: Incident details
During a routine inspection of ‘open drain’ pipework on WPP cellar deck (North) by TRAC personnel, a decommissioned 4” spool 3.5m long was discovered unsecure and at height – a potential dropped object. (Note: The length of time this had been in this position is not known.)
After the appropriate procedures had been followed to retrieve the spool safely to deck, it was agreed that further investigations be carried out on the WPP by rope access technicians to identify if there were any further potential dropped objects located on piperacks / cable trays etc.
The following photographs identify what was found…….

## Slide 3
Spool (once lowered to deck)

## Slide 4
Items found on WPP
piperacks/ cable trays
on MEZZ DECK
Items found on WPP
piperacks/ cable trays
on CELLAR DECK

## Slide 5: Dropped Object Potential
DROPS CALCULATOR IS A GUIDE ONLY providing cursory indication of possible outcome
With light objects (<0.1 kg) a key influencing factor is the effect of an object punching the skin and damaging tissue/organic functions. The calculator assumes a blunt object so is not compatible with broken glass, metal shards etc
The wearing of standard PPE, eg hard hat, safety boots and eye protection, is assumed in the calculator.

## Slide 6: Key Lessons
When comparing some of the items found with the drops calculator, many had the potential for serious injury or fatality if they had dropped.
REMEMBER
Check your worksites before you leave/complete the job – do you have all the tools/equipment etc you started with?
If you accidentally drop something (e.g. onto a cable tray or piperack), don’t leave it. Report it to your supervisor who will request rope access technicians to retrieve any unsecured items/potential dropped objects
Tenet 8: Address abnormal conditions
THINK

## Slide 7: CAPTAIN FPSO
Safety Reps/Volunteers have become more involved with the DROPS process and have been on the training course.
Hopefully DROPS will be aligned with CHEVRON’s New Area Ownership procedure that is currently under review.

## Slide 8: CAPTAIN FPSO Incident during bad weather